## Slide 1: Dipartimento di Elettronica, Informazione e Bioingegneria
AI@Edge in Biomedical Applications
Anna Maria Stucchi - 10797657
Milano, agosto 2025
2025

## Slide 2: AI@Edge in Biomedical Applications Accelerators for Machine Learning on Embedded Devices
Introduction & motivation
Background: Edge AI and accelerators
Main hardware platforms
Lightweight networks & software tools
Biomedical applications
Challenges and future trends
Conclusions & repository

## Slide 3: Introduction & Motivation What is Edge AI?
Edge AI = deployment of machine learning models on embedded/edge devices
Operates close to the data source (e.g., sensors, cameras, wearables)
Complements cloud computing → reduces latency, improves privacy and bandwidth efficiency

## Slide 4: Introduction & Motivation Why in Biomedical Applications?
Real-time requirements:
  Emergency diagnostics (ambulances, ICU)
  Continuous monitoring of chronic patients
Data sensitivity:
  Patient health data must remain local (HIPAA/GDPR compliance)
Accessibility:
  Portable and affordable AI devices → broader access to healthcare

## Slide 5: Introduction & Motivation Market & Research Trends
Global Edge computing in healthcare market:
  Valued at USD 5.28B in 2023, expected to reach USD 12.9B by 2028 (CAGR 26.1%)
Increasing adoption of AI-based medical devices (Intel, NVIDIA, Apple, Google TPU)
Research shift: from cloud-only AI → towards edge + AI co-design

## Slide 6: Introduction & Motivation
Healthcare is moving towards point-of-care (medical tests performed at or near the patient's location) diagnostics and remote monitoring
Embedded AI accelerators enable:
Fast inference
Low-power consumption
On-device medical applications

## Slide 7: Background: Edge AI and Accelerators Edge AI: Concept
Definition: Deployment of deep learning networks (DNN) on edge devices (close to data sources such as sensors, wearables, cameras), bringing artificial intelligence closer to the data source
Benefits over cloud computing:
Low latency
Privacy and data protection
Reduced bandwidth usage
Key enablers: IoT, 5G, efficient ML accelerators

## Slide 8: Background: Edge AI and Accelerators Challenges
Resource constraints: limited CPU/GPU, memory, power
Large models (CNNs, Transformers) are too heavy for microcontrollers
Heterogeneity of hardware/software → portability issues
Standardization and regulatory barriers in medical devices

## Slide 9: Background: Edge AI and Accelerators What are ML Accelerators?
Definition: Hardware specifically designed to speed up AI inference/training tasks
Main categories:
ASICs (e.g., Google Edge TPU, Apple Neural Engine)
FPGAs (flexible, reconfigurable, good for prototyping)
GPUs (general-purpose parallel processing, e.g., NVIDIA Jetson)
Memristor-based / Neuromorphic chips (next-gen, energy efficient)
Key features: throughput (TOPS), latency, power efficiency, programmability

## Slide 10: Background: Edge AI and Accelerators Classification of Edge Devices
Low-end: microcontrollers (e.g., STM32, SparkFun Edge) → wearables, lightweight inference
Medium-range: boards (e.g., Raspberry Pi + NCS2, Google Coral Dev Board, Jetson Nano) → portable medical imaging, pathology screening
High-performance: Jetson Xavier, Orin, workstations → real-time CT/MRI analysis, robotics in surgery

## Slide 11: Background: Edge AI and Accelerators Classification of Edge Devices

## Slide 12: Background: Edge AI and Accelerators Relevance to Biomedical Applications
Wearable sensors: continuous monitoring of ECG/EEG/EMG
Portable diagnostic devices: ultrasound, dermatology cameras, retinal screening
Critical care: ICU patient monitoring, telemedicine in remote areas
Accelerators enable near real-time inference with low power and high reliability

## Slide 13: Main Hardware Platforms Overview
Hardware accelerators enable real-time, low-power inference on embedded devices
Categories:
ASICs (fixed-function, very efficient)
FPGAs (reconfigurable, versatile)
GPUs/NPUs (high throughput, flexible)
Memristor/Neuromorphic (emerging hardware, bio-inspired)
Each platform offers a different trade-off:
performance vs. flexibility vs. energy

## Slide 14: Main Hardware Platforms Why specialized Accelerators?
CPUs are general-purpose → inefficient for deep learning
Accelerators exploit parallelism in matrix operations
Goal: high throughput, low latency, low energy per inference
Accelerators implement:
  MAC arrays (Multiply-Accumulate units)
  Low-precision arithmetic (8-bit, 4-bit, even binary ops)
  On-chip memory to reduce data transfer costs

## Slide 15: Main Hardware Platforms Key Performance Metrics
TOPS (Tera Operations per Second) → raw compute
TOPS/Watt → energy efficiency
Latency → time to process one inference
Memory bandwidth → critical for large models
Programmability → flexibility vs. fixed hardware

## Slide 16: Main Hardware Platforms ASIC Accelerators
Examples: Google Edge TPU, Apple Neural Engine (ANE), ARM Ethos-U NPU
Advantages: ultra-low power, small form factor, optimized for inference
Limitations: fixed functionality, less flexible for new models
Biomedical use cases:
Portable retinal imaging (Edge TPU)
Wearable ECG analysis (ANE in Apple Watch)

## Slide 17: Main Hardware Platforms ASIC Accelerators: Google Edge TPU
Optimized for 8-bit quantized TensorFlow Lite models
4 TOPS at <2 W → very energy efficient
Used in Coral Dev Board (diagnostic cameras, IoT healthcare)
Limitation: no floating-point, less flexibility

## Slide 18: Main Hardware Platforms ASIC Accelerators: Apple Neural Engine (ANE)
Integrated in iPhones & Apple Watch
Handles biometric authentication and ECG anomaly detection
16-core engine, ~17 TOPS (iPhone 14 Pro)
Highly optimized for health-oriented apps

## Slide 19: Main Hardware Platforms FPGA-based Accelerators
Reconfigurable hardware → customizable for specific AI tasks
Tools: OpenCL, High-Level Synthesis, Vitis AI
Advantages: flexibility, energy efficiency, prototyping new models
Limitations: programming complexity, less mature software ecosystem
Biomedical use cases:
EEG/ECG anomaly detection
EMG-based prosthetic control
Portable ultrasound image processing

## Slide 20: Main Hardware Platforms FPGA-based Accelerators: Xilinix Zynq
Customizable pipelines for CNN/ECG/EEG
Toolchains: Vitis AI, High-Level Synthesis
Advantage: can adapt architecture to medical task
Limitation: longer development cycle

## Slide 21: Main Hardware Platforms FPGA Case Study in Biomedicine
EMG classification for prosthetic control
FPGA provided 20× lower latency vs CPU
Demonstrated feasibility for real-time prosthetics
Trade-off: development complexity

## Slide 22: Main Hardware Platforms GPU & NPU Platforms
Embedded GPUs: NVIDIA Jetson Nano, Xavier, Orin → high parallelism, full DL frameworks (TF, PyTorch, ONNX)
NPUs (specialized processor designed to accelerate computations needed for AI): Qualcomm Hexagon DSP, Huawei Ascend → optimized for mobile inference
Advantages: flexibility, strong software support
Limitations: higher power consumption
Biomedical use cases:
MRI/CT real-time segmentation (Jetson Orin)
Smartphone-based medical imaging with NPUs

## Slide 23: Main Hardware Platforms GPU for Edge: NVIDIA Jetson Family
Jetson Nano → 0.5 TFLOPS, entry-level
Jetson Xavier NX → 21 TOPS, balance of power/efficiency
Jetson Orin → up to 200 TOPS, advanced imaging tasks
Supports full DL frameworks (TF, PyTorch, ONNX)

## Slide 24: Main Hardware Platforms GPU Case Study in Medical Imaging
Jetson Xavier used for MRI segmentation
Achieved real-time inference with <250 ms latency
Applications: CT anomaly detection, ultrasound analysis

## Slide 25: Main Hardware Platforms Memristor & Neuromorphic Accelerators
Memristors: enable in-memory computing → lower latency, energy efficiency
Neuromorphic chips: IBM TrueNorth, Intel Loihi → inspired by brain networks
Advantages: ultra-low power, suitable for biomedical sensors and implants
Challenges: device variability, limited maturity, standardization issues
Biomedical use cases:
EMG/EEG signal classification (prototypes)
Spiking neural networks for prosthetics & brain-computer interfaces

## Slide 26: Main Hardware Platforms Memristor Accelerators
In-memory computing → reduces data movement
Advantages: low power, high parallelism
Used in MDNN (Memristor-based DNNs)
Tools: MemTorch (open-source simulation)
Challenge: device variability & reproducibility

## Slide 27: Main Hardware Platforms Neuromorphic Computing
Chips inspired by the brain: spiking neural networks (SNNs)
Intel Loihi, IBM TrueNorth
Ultra-low-power, event-driven processing
Applications: continuous EEG/ECG monitoring, implants
Challenge: not yet mainstream in clinical devices

## Slide 28: Main Hardware Platforms Comparison Table (general)
Platform | Examples | Pros | Cons | Biomedical Use
ASIC | Edge TPU, ANE | Low power, efficient | Fixed function | Wearables, mobile diag.
FPGA | Xilinx Zynq, Intel Stratix | Reconfigurable, efficient | Complex programming | EEG/ECG, prosthetics
GPU/NPU | Jetson, Qualcomm DSP | Flexible, strong SW support | High power | Imaging, real-time diag.
Memristor/Neuromorphic | Loihi, MemTorch | Ultra-low power, bio-inspired | Immature, limited support | BCI, implants

## Slide 29: Main Hardware Platforms Comparison Table
Accelerator | Example | Perf (TOPS) | Power | Biomedical Use
ASIC | Google Edge TPU | 4 | <2W | Retinal imaging, wearables
ASIC | Apple Neural Engine | 17 | Smartphone power budget | ECG detection
FPGA | Xilinx Zynq | Custom | 5–10W | EMG prosthetics, EEG
GPU | Jetson Xavier NX | 21 | 10–15W | MRI/CT, ultrasound
GPU | Jetson Orin | 200 | 25–50W | Robotics, advanced imaging
Memristor | MDNN proto | — | mW range | In-memory ML (research)
Neuromorphic | Intel Loihi | — | Ultra-low | EEG, implants

## Slide 30: Lightweight Models & Software Tools Why lightweight Models?
Transferring large DNNs to lightweight DNNs
Edge devices → limited memory, power, compute capacity
Standard CNNs (ResNet, VGG) too large for microcontrollers
Need compression & efficient architectures for on-device ML

## Slide 31: Lightweight Models & Software Tools Techniques for Model Optimization
Pruning (remove redundant neurons/weights)
Quantization (reduce precision, e.g., 32-bit → 8-bit)
Sparse representation
Neural Architecture Search (NAS)
Knowledge distillation (transfer learning from large → small models)

## Slide 32: Lightweight Models & Software Tools Lightweight Architectures
Nowadays many neural network architectures are lightweighted by design rather than reducing a given large network.
MobileNet (V1–V3) – efficient CNN for mobile devices (used in diagnostic instruments)
EfficientNet – compound scaling for accuracy & efficiency
ShuffleNet, SqueezeNet, GhostNet – ultra-low resource use (group convolutional networks)
Mobile Transformers (MobileViT, EdgeViT) – balance accuracy & latency

## Slide 33: Lightweight Models & Software Tools Software frameworks
TensorFlow Lite – inference on microcontrollers
PyTorch Mobile / ExecuTorch – optimized for smartphones
ONNX Runtime – portability across accelerators
OpenVINO (Intel) – optimized inference on CPUs/VPUs
NVIDIA Triton – deployment across Jetson devices

## Slide 34: Biomedical Applications Medical Imaging
Portable ultrasound with Edge AI
Retinal fundus screening for diabetic retinopathy
X-ray anomaly detection (pneumonia, fractures) on mobile devices

## Slide 35: Biomedical Applications Wearable Devices
ECG monitoring with real-time anomaly detection
EEG/EMG analysis for neuroprosthetics
Smartwatches detecting arrhythmias

## Slide 36: Biomedical Applications Point-of-Care Devices
AI-enabled diagnostic kits for rural/low-resource settings
Edge AI for emergency care (ambulances, portable scanners)
Reduces dependency on cloud → more autonomy

## Slide 37: Challenges & Limitations Technical Challenges
Limited compute, memory, energy vs. large DL models
Hardware heterogeneity → portability issues
Lack of standardized APIs across accelerators

## Slide 38: Challenges & Limitations Biomedical-Specific Challenges
Data privacy & regulation (HIPAA, GDPR)
Validation & certification of AI-powered medical devices
Accuracy trade-offs in lightweight models for critical tasks

## Slide 39: Challenges & Limitations Economic & Market Barriers
High costs for high-performance accelerators
Limited availability in low-resource healthcare systems
Need for scalable, affordable solutions

## Slide 40: Future Trends Neuromorphic & Memristor-Based AI
Brain-inspired accelerators for ultra-low-power computation
Suitable for implantable or continuous-monitoring medical devices
Still early-stage → research prototypes

## Slide 41: Future Trends Federated & On-Device Learning
Training directly on local devices → improved personalization
Preserves privacy (no raw data transfer)
Example: collaborative ECG/EEG learning across wearables

## Slide 42: Future Trends Integration with Healthcare Systems
Hybrid cloud–edge architectures
Standardization & regulatory frameworks needed
Edge AI as a complement, not a replacement, of cloud AI

## Slide 43: Conclusion
Edge AI enables real-time, private, efficient biomedical applications
Hardware accelerators (ASIC, FPGA, GPU, memristors) are central
Lightweight models + optimized frameworks make deployment feasible
Combination of hardware innovation + lightweight models will shape future medical devices
Still open: standardization, validation, certification

## Slide 44: References
Repository with slides and sources
https://github.com/annastucchi/desk-research-ai-edge-biomedical/tree/main
[1] Rahimi et al. (2020) - https://arxiv.org/abs/2007.05657
[2] Xu et al. (2025) - https://link.springer.com/article/10.1007/s10462-024-11033-5
[3] Google Coral Benchmarks - https://coral.ai/docs/edgetpu/benchmarks/
[4] NVIDIA Jetson Orin Nano - https://developer.nvidia.com/blog/solving-entry-level-edge-ai-challenges-with-nvidia-jetson-orin-nano/
[5] DeepEdgeBench (Blott et al., 2021) - https://arxiv.org/abs/

## Slide 45
Anna Maria Stucchi
Master’s student in computer engineering
CONTACT
annamaria.stucchi@mail.polimi.it